## Slide 1: Cortex M4
Girish S Kumar
Notes: Click to add notes

## Slide 2: Cortex M4 General View
A 32 Bit microcontroller
It is designed to achieve
    High code density,
    Fast interrupt response times
    Signal processing Algorithms
    IEEE floating-point units
    Real time Operating System support
    Advance Trace Capabilities
Notes:   How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
  Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 3
Processor Modes
Cortex –M4 has two modes
Thread Mode
Handler mode
Processor Mode | What happens in this mode
Thread mode | All User Application executes in this mode, when processor is RESET and completes the reset process, it automatically comes to Thread mode
Handler mode | All Exceptions are handled in this mode, once the exception handling is completed it goes back to thread mode

## Slide 4: Privileges in Mode
 | Privilege Mode | What can a program do in the mode
1 | Privileged mode | No Restrictions – Full access to everything
2 | Unprivileged mode | A program in this mode has limited access the xPSR register or it flags through MRS and MSR instructions Cannot access system timer, Nested Vectored Interrupt Controller (NVIC) , system control block May have restricted access to memory or peripherals.
Notes: Lesson descriptions should be brief.

## Slide 5: Processor Mode and Privileges
Use of this mode:
Exception Handling
Stack : Main
Use of this mode:
Applications use this mode
Under special conditions
Stack : Main or process
Use of this mode:
Applications will be in this mode most of the time
Stack : Main or process
Handler
mode
Thread
mode
Privileged
User
Privileged
User
Thread
mode
Processor mode
Privileges
Notes: Example objectives
At the end of this lesson, you will be able to:
  Save files to the team Web server.
  Move files to different locations on the team Web server.
  Share files on the team Web server.

## Slide 6: Registers in Cortex-M4

## Slide 7
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(SP)
R14 (LR)
R15(PC)
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
MSP
PSP
Banked Version
General
Purpose
Registers
Low Registers
High Registers
Program Status Register
Control Register
Exception Register
Special Purpose Registers

## Slide 8: Stacks in ARM processor

## Slide 9: Types of Stack
Ascending Stack:
In a push the stack pointer is incremented, i.e the stack grows towards higher address.
Descending Stack:
In a push the stack pointer is decremented, i.e the stack grows towards lower address.
Ascending Empty stack
Stack pointer points to the location in which the next item will be stored. A push will store the value, and increment the stack pointer.
Ascending Full Stack
Stack pointer points to the location in which the last item was stored. A push will increment the stack pointer and store the value.
Descending Empty stack
Stack pointer points to the location in which the next item will be stored. A push will store the value, and increment the stack pointer.
Full stack
Descending Full Stack
Stack pointer points to the location in which the last item was stored. A push will increment the stack pointer and store the value

## Slide 10
The Cortex M4 uses a full descending stack. This means the stack pointer holds the
address of the last stacked item in memory.
The processor implements two stacks, the main stack and the process stack, with a pointer for each held in independent registers,
Stack on Cortex M4
Processor Mode | Used to execute | Privilege level | STACK USED
Thread | Applications | Privileged or Un privileged | Process stack or Main stack Based on CONTROL Register
Handler | Exceptions | Always Privileged | Main Stack
R13(SP)
MSP
PSP
Main Stack
Process stack

## Slide 11
CONTROL Register
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
The CONTROL is a 32 bit register, that controls the
Which stack used at a given time
When the processor is in Thread mode it decides the privilege level
Indicates whether the Floating point Unit is active
BITS | Name | Function
31 …… 3 Bits | No name | Reserved
2 | FPCA | 0 = no floating-point context active 1 = floating-point context active.
1 | SPSEL | 0 = MSP is the current stack pointer 1 = PSP is the current stack pointer.
0 | nPRIV | Defines the Thread mode privilege level: 0 = privileged 1 = unprivileged.

## Slide 12
Program Status Register (PSR) Cortex M4
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 20 | 19 | 16 | 15 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
N | Z | C | V | Q |  |  |  |  |  | G.. | ..E |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | ICI/IT |  | T |  |  |  | ICI/IT |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | ISR NUMBER |  |  |  |  |  |  | 
APSR
EPSR
IPSR
4 Bits

## Slide 13
The APSR contains the status flags (N, C, V, and Z), the Greater Than or Equal flags (used by the SEL instruction), and an additional “sticky” Q flag used in saturation arithmetic, where sticky in this case means that the bit can only be cleared by explicitly writing a zero to it.
BITS | NAME | FUNCTION
31 | N | Negative Flag
30 | Z | Zero Flag
29 | C | Carry or Borrow Flag
28 | V | Overflow Flag
27 | Q | DSP Overflow and Saturation Flag
26:20 | - | Reserved
19:16 | GE[3:0] | Greater than or Equal flags for SEL instruction
15:0 | - | Reserved
APSR Bit assignments
Application Program Status Register (APSR),

## Slide 14
SEL Instruction
The SEL instruction:
1. Reads the value of each bit of APSR.GE.
2. Depending on the value of APSR.GE, assigns the destination register the value of
either the first or second operand register.
Examples
SADD16 R0, R1, R2 ; Set GE bits based on result
SEL R1, R0, R3 ; Select bytes from R0 or R3 and assign to to R1, based on GE.

## Slide 15
IPSR contains only an exception number that is used in handling faults and other types of exceptions.
Interrupt Program Status Register (IPSR)
BITS | NAME | FUNCTION
[31:9] | - | Reserved
[8:0] | ISR NUMBER | This is the number of the current exception: 0 = Thread mode 1 = Reserved 2 = NMI 3 = HardFault 4 = MemManage 5 = BusFault 6 = UsageFault 7-10 = Reserved 11 = SVCall 12 = Reserved for Debug 13 = Reserved 14 = PendSV 15 = SysTick 16 = IRQ0. . . . n+15 = IRQ(n-1)a

## Slide 16
Two fields contain the IF-THEN instruction status bits overlapped with the
Interrupt-Continuable Instruction (ICI) bits, PLUS the Thumb (T) bit
Execution Program Status Register (EPSR)
BITS | NAME | FUNCTION
[31:27] | - | Reserved
[26:25], [15:10] | ICI | Interruptible-continuable instruction bits
[26:25], [15:10] | IT | Indicates the execution state bits of the IT instruction. (To be discussed Later)
[24] | T | Thumb state bit. (To be discussed Later)
[23:16] | - | Reserved
[9:0] | - | Reserved

## Slide 17
When an interrupt occurs during the execution of an LDM, STM, PUSH, or POP instruction, and when
an FPU is implemented an VLDM, VSTM, VPUSH, or VPOP instruction, the processor:
• stops the load multiple or store multiple instruction operation temporarily
• stores the next register operand in the multiple operation to EPSR bits[15:12].
After servicing the interrupt, the processor:
• returns to the register pointed to by bits[15:12]
• resumes execution of the multiple load or store instruction.
When the EPSR holds ICI execution state, bits[26:25,11:10] are zero.
What are Interruptible-continuable instructions

## Slide 18
Exception Registers Cortex M4
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL

## Slide 19: PRIMASK
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
The PRIMASK register prevents activation of all exceptions with configurable priority.
BIT | NAME | FUNCTION
[31:1] | - | Reserved
0 | PRIMASK | 0 = no effect 1 = prevents the activation of all exceptions with configurable priority

## Slide 20: FAULT MASK
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
The FAULTMASK register prevents activation of all exceptions except for Non-Maskable Interrupt (NMI).
BIT | NAME | FUNCTION
[31:1] | - | Reserved
0 | FAULTMASK | 0 = no effect 1 = prevents the activation of all exceptions except for NMI.

## Slide 21
BASEPRI
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
The BASEPRI register defines the minimum priority for exception processing. When BASEPRI is set to a nonzero value, it prevents the activation of all exceptions with the same or lower priority level as the BASEPRI value
BIT | NAME | FUNCTION
[31:1] | - | Reserved
0 | FAULTMASK | Priority mask bits: 0x00 = no effect Nonzero = defines the base priority for exception processing. The processor does not process any exception with a priority value greater than or equal to BASEPRI.

## Slide 22
Register Summary
Name | Type | Required Privilege
[R0-R12] | RW | Either
MSP | RW | Privileged
PSP | RW | Either
LR | RW | Either
PC | RW | Either
PSR | RW | Privileged
APSR | RW | Either
IPSR | RO | Privileged
EPSR | RO | Privileged
PRIMASK | RW | Privileged
FAULTMASK | RW | Privileged
BASEPRI | RW | Privileged
CONTROL | RW | Privileged

## Slide 23
Floating Point Processing
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(SP)
R14 (LR)
R15(PC)
PSR
PRIMASK
FAULTMASK
BASEPRI
CONTROL
MSP
PSP
Banked Version
General
Purpose
Registers
Low Registers
High Registers
Program Status Register
Control Register
Exception Register
Special Purpose Registers
32 single-precision floating-point registers (s0–s31) or 16 double-precision
registers (d0–d15) or a mix
S0
S1
S2
S3
S30
S31
D0
D1
D15

## Slide 24
What is IEEE Single Precision and Double Precision ?
The IEEE single precision floating point standard representation requires a 32 bit word
which may be represented as numbered from 0 to 31, left to right.
The 0th is the sign bit, S,
the next eight bits [1:8] are the exponent bits, 'E', and
the final 23 bits are the fraction 'F':
The IEEE double precision floating point standard representation requires a 64 bit word
which may be represented as numbered from 0 to 63, left to right.
The first bit is the sign bit, S,
The next eleven bits are the exponent bits, 'E', and
The final 52 bits are the fraction 'F':

## Slide 25: Vector Table
The Cortex-M4 vector table is probably one of the larger departures from all previous ARM processor designs. Returning to the idea that addresses are stored in the vector table, rather than instructions,
Exception Type | Exception No | Address
(Top of Stack) | ------------ | 0x00000000
Reset | 1 | 0x00000004
NMI | 2 | 0x00000008
Hard Fault | 3 | 0x0000000C
Memory management fault | 4 | 0x00000010
Bus Fault | 5 | 0x00000014
Usage Fault | 6 | 0x00000018
SV Call | 11 | 0x0000002c
Debug monitor | 12 | 0x00000030
Pend SV | 14 | 0x00000038
Sys Tick | 15 | 0x0000003c
Interrupts | 16 and above | 0x00000040 and above

## Slide 26: References
http://stackoverflow.com/questions/801117/whats-the-difference-between-a-single-precision-and-double-precision-floating-p