## Slide 1: Stacks and Subroutines
Girish S Kumar

## Slide 2: Sub Routines
Subroutine allows programmers to break the code into smaller chunks
How does subroutine works
When a subroutine is called with BRANCH and LINK instruction,
The control will be transferred to the first instruction of the subroutine
The address of the instruction to which control has to come will be saved in Linked Registered (R14)
MAIN
BL subRoutine1
CMP R3,R4
subRoutine1
BL subRoutine2
MOV R3, R1
BX lr
subRoutine2
BX lr

## Slide 3: Passing Parameters through Registers
Easiest way to exchange parameters & results to Subroutine is to use registers
In case any of the registers are impacted by subroutine, make sure that those registers are saved on to the stack before calling the subroutine
However large quantities (large blocks) of data cannot
be exchanged using this method.

## Slide 4: Passing Parameters through Reference
When we need to exchange a list of values to subroutine, registers cannot be used. So the practical approach is copy the values that need to passed to a subroutine or returned to the calling program into a memory location (Block of RAM) and we exchange just the start address of the block. As RAM is read and write for everyone, the calling routine as well as called routine can modify the read and modify the data in block

## Slide 5: Passing by Reference
Main
Subroutine1
10 | 21 | 56 | 38 | ……………………..
Address is passed

## Slide 6: Passing Parameters on Stack
Alternatively we can use stack itself to pass parameters to Subroutine, this one he most straight forward methods as SP is only entity needed for this.
Before a subroutine is called all the parameters are pushed on to stack
The subroutine get the parameters off the stack by pop-ing
Process the data
Push the results back to stack
Upon return the main program get the results by pop-ing the stack

## Slide 7: ARM APCS
The criteria we have considered to be important are:
* Function call should be fast and it should be easy for compilers to
optimise function entry sequences.
* The function call sequence should be as compact as possible.
* Extensible stacks and multiple stacks should be accommodated.
* The standard should encourage the production of reentrant code, with
writable data separated from code.
* The standard should be simple enough to be used by assembly language
programmers, and should support simple approaches to link editing,
debugging and run-time error diagnosis.
Overall, we have tended to rank compact code and a clear definition most
highly, with simplicity and ease of use ahead of performance in matters of fine
detail where the impact on performance is small.

## Slide 8: Usage of Registers
The first four registers r0-r3 (also called a1-a4, for argument) are used to pass
argument values into a subroutine and to return a result value from a function.
They may also be used to hold intermediate values within a routine
(but in general, only between subroutine calls).
Register r12 (IP) may be used by a linker as a scratch register between a routine
and any subroutine it calls. It can also be used within a routine to hold
intermediate values between subroutine calls.
Typically, the registers r4-r8, r10, and r11 are used to hold the values of a routine’s local variables. Of these, only r4-r7 can be used uniformly by the whole Thumb instruction set, but the AAPCS does not require that Thumb code only use those registers.
A subroutine must preserve the contents of the registers r4-r8, r10, r11, and SP
(and r9 in some Procedure Call Standard variants). The ARM and Thumb C and C++ compilers always use a full descending stack.
SP mod 4 = 0. The stack must at all times be aligned to a word boundary.
SP mod 8 = 0. The stack must be double-word aligned